## Slide 1: F-35 Capabilities Slides: Unclassified
Capt Shaun “MOBY” Dickinson

## Slide 2: Overview
State of the F-35A
Aircraft Capabilities

## Slide 3: F-35 Multi-role Strike Fighter
Goal: 80% commonality across variants
  Common airframe, hardware/software, maintenance, and training
  Future upgrades and software updates more easily incorporated
  Allows more efficient test and checkout procedures

## Slide 4: Variant Comparison
CTOL
Folded Span 31.1 ft
F-16
AV-8B
F/A-18C
Weight Empty (lb) 29,036
Internal Fuel (lb) 18,480
Weight Empty (lb) 32,161
Internal Fuel (lb) 14,003
Span (ft) 35
Length (ft) 51.4
Wing Area (ft2) 460
Span (ft) 35
Length (ft) 51.1
Wing Area (ft2) 460
Span (ft) 43
Length (ft) 51.4
Wing Area (ft2) 668
Weight Empty (lb) 32,072
Internal Fuel (lb) 20,085
Wing Fold
Gun Fairing
Lift Fan Fairing
CV
STOVL

## Slide 5: LO Design
Aircraft Shaping
Weapons Carried Internally
Embedded Antennas
Low-Emission Radar and Avionics
Low Observable Seams
DISTRIBUTION STATEMENT A: Approved for public release; distribution is unlimited

## Slide 6: Cockpit Overview Comparison
Next-Generation Cockpit
  20" x 8" interactive display
  Helmet-mounted display/virtual HUD
  Pilot-oriented information presentation

## Slide 7: Cockpit Overview F-35 Layout
20” x 8” Contiguous Display
Center Pedestal
Left Console Panel
Stick and Throttle
Services Connection Panel
ICC / IPP Panel
Left Auxiliary Console
Right Auxiliary Console

## Slide 8: Cockpit Displays Configurable Display Concept

## Slide 9: Cockpit Displays Configurable Display Concept
Portal control
Pilot configurable
Master Modes

## Slide 10: Cockpit Displays Virtual Data Entry Device (vDED)

## Slide 11
Sidestick
Weapons Release Enable (Pickle) Switch
Target Management Switch (TMS)
Trim Switch
Display Management Switch (DMS)
Electronic Warfare Switch (EWS)
Zoom/Expand FOV
Adjustable Hand Rest
Sidestick
(View From Back)

## Slide 12
Throttle Grip
Cage/Uncage
Weapon Management
Switch (WMS)
Cursor Slew
Controller
Speed Brake
Flare
External Lights
MPO
Throttle Grip
(View From Top)

## Slide 13: Throttle Grip
Cage/Ungage
APC
Communication Control
& Voice Recognition (VR)
Management Switch
Speed Hold
Polarity Control
External Lights
Throttle Grip
(View From Front)

## Slide 14: Helmet Mounted Display (HMD) Symbology
Air-to-Air
Symbology
Friendly Air
Symbology
Air-to-Surface
Symbology
18L

## Slide 15: APG-81 Radar Advanced Electronically Scanned Array
Lockheed Martin Aeronautics Company
DISTRIBUTION STATEMENT A. Approved for public release; distribution is unlimited.
Air-to-Air Target Engagement
Synthetic Aperture RADAR
Ground Moving Target Detection
Air-to-Air Target Detection/Track
Electronic Attack/
High Gain ESM
Sea Surface
Detection
JSF Approved General Briefing Oct 2003 - 15

## Slide 16: SAR Maps
Legacy Resolution
JSF APG-81 Resolution
DISTRIBUTION STATEMENT A: Approved for public release; distribution is unlimited

## Slide 17: Integrated Avionics Suite
Full Spherical Coverage by Distributed Aperture System
Fwd Band 2
Aft Band 2
RADAR
Array &
Electronics
Fwd Band 3/4
RWR
360 Deg Coverage
Fwd Band 2
DAS Apertures
Band 3/4
Radar Warning
Band 3/4
Radar Warning
SATCOM
Data Links
Fwd Band 3/4
EO
Targeting
System
ESM
Emitter Locating
RADAR

## Slide 18
Left Side
Lower Forward
Upper Aft
Lower Aft
Upper
Forward
3
4
1
2
5
6
Distributed Aperture System (DAS) Sensor Array

## Slide 19: Distributed Aperture System
Internally Mounted
Missile Launch Detection
Threat Aircraft Detection
Track Wingman
NAVFLIR Functions
Integrated With HMD
Notes: Replaces Night Vision Devices
Sees everything worlds best RIO

## Slide 20: Capabilities DAS Missile Warning Symbology

## Slide 21: Electro-Optical Targeting System (EOTS) Capabilities
Laser Spot Tracker
Long Range A-A IRST
Lockheed Martin Aeronautics Company
DISTRIBUTION STATEMENT A. Approved for public release; distribution is unlimited.
Air-to-Surface
Targeting FLIR
Air-to-Air Targeting FLIR
Laser
Designation
JSF Approved General Briefing Oct 2003 - 21

## Slide 22: Electro-Optical Targeting System (EOTS) Sensor Location
Sensor/Window Installation
Seven Sapphire Faceted Window Configuration
110º
EOTS
Notes: Sniper 3.0
Block 4 upcoming,

## Slide 23
Identification/Surveillance
Mark XII Transponder
Mark XII Interrogator
Audio Functions
Voice Messaging
Voice Recognition (Support)
Air Refuel Intercom (CTOL)
Maintenance Intercom
Active Noise Reduction
Data Communications
Link 16
Link 16 Enhanced Throughput
MADL (JSF Wideband)
Weapon Data Link (AWW-13)
Navigation/Landing Aids
INS
GPS
Radar Altimeter
ILS Marker Beacon
ILS Glideslope
ILS Localizer
TACAN
Carrier ILS
MLS (w/DME-P)
JPALS*
Voice Communications
VHF Lo-FM (30-88 MHz)
VHF AM (108-156 MHz)
VHF Hi-FM (136-174 MHz)
UHF AM (225-400 MHz)
UHF FM (225-400 MHz)
Havequick
SINCGARS
GUARD Monitor (243/121.5)
KY-58 Secure Voice
Data Message Formats
TADIL-J
JVMF / VMF (K-series)
TADIL-C (partial)
OTCIXS-II
OTH-Gold
TACFIRE
AFAPD
Communication, Navigation, ID (CNI) Capabilities

## Slide 24: CTOL Weapons Carriage Requirements
CTOL Internal Gun
Store Fully Certified During SDD
Stormshadow
GBU-16 Paveway II 1,000-lb LGB (MK-83 Warhead)
AIM-9X Sidewinder
MK-84 BSU-50 Ballute 2,000-lb HDGP
GBU-24A/B Paveway III 2,000-lb LGB (MK-84 / BLU-109 Warhead)
CBU-99/100 Rockeye II
Cluster Munition
426 -Gallon Wing Tank
GBU-10 Paveway II 2,000-lb LGB (MK-84 Warhead)
MXU-648/CNU-88 Baggage Pod
BDU-57/58/60
Laser-Guided Training Round
AGM-158 JASSM
EXTERNAL WEAPONS
EXTERNAL WEAPONS
INTERNAL
MK-82 500-lb LD & HD
GBU-12 Paveway II 500-lb LGB
(MK-82 Warhead)
AIM-120B/C AMRAAM
AIM-120C AMRAAM
Brimstone/Joint
Common Missile
GBU-12 Paveway II 500-lb LGB
(MK-82 Warhead)
GBU-31 JDAM 2,000-lb
(MK-84 Warhead)
AGM-154A/C JSOW Glide Bomb
GBU-31 JDAM 2,000-lb
(BLU-109 Warhead)
AIM-132 ASRAAM
Brimstone/Joint
Common Missile
GBU-32 JDAM 1,000-lb
(MK-83/BLU-110 Warhead)
CBU-103/105 WCMD
Missionized Gun
UK 500# PGB
Phase I SDB
GBU-38 JDAM 500-lb
(MK-82 Warhead)
MK-83 BSU-85 HDGP
MK-84 2,000-lb LD/HDGP
MK-83 BLU-110 LDGP 1,000-lb LDGP
Weapons Currently Under Development
AGM-154A/C JSOW Glide Bomb
GBU-31 JDAM 2,000-lb
(MK-84 Warhead)
MK-76/MK-58/BDU-48
GBU-32 JDAM 1,000-lb
(MK-83/BLU-110 Warhead)
GBU-31 JDAM 2,000-lb
(BLU-109 Warhead)
CBU-103/105 WCMD
AIM-132 ASRAAM
GBU-38 JDAM 500-lb
(MK-82 Warhead)
DISTRIBUTION STATEMENT A. Approved for public release; distribution is unlimited.
Notes: External Weapons
Change 480 gallon wing tank to 426 gallon wing tank
Add AIM-120B AMRAAM
Update Missionized Gun image
Make font color change to denote only MK-82 500lb LD is certified in SDD
Internal/External Weapons
Removed CBU-87/89/97 Cluster Munitions
Removed JDAM PIP

## Slide 25: Weapons Bays Airframe Orientation
Internal Weapons Bays

## Slide 26: Components Doors
CTOL and CV variants share same bay and can carry 2000 lb weapons
STOVL has a smaller bay and is limited to 1000 lb class weapons
CTOL
STOVL

## Slide 27: Components Doors
Two operational modes
  Ground = 10-15 seconds open/close
  Inflight = 2.4 seconds open/close
27
In Flight Operations
Ground Operations
Notes: <insert time>

## Slide 28
4 internal weapons stations (similar on all variants)
  Stations 4 & 8 (outboard, internal) can carry either air-to-surface stores or air-to-air missiles
  Stations 5 & 7 (inboard, internal) can carry air-to-air missiles
Weapons Stations Station Designation & Specifications
4
8
5
7

## Slide 29
Seven external weapons stations (similar on all variants)
  Stations 3 and 9 carry 5000-lb stores or fuel
  Stations 2 and 10 carry 1000-lb stores
  Centerline station (6) can carry missionized gun only
  Remaining 2 stations (1 and 11) can carry AIM-9X or AIM-132 ASRAAM missiles
1
2
11
10
6
9
3
Weapons Stations Station Designation & Specifications

## Slide 30: Gun System Components & Operation
Internal Gun
  181-round Ammunition Handling System (AHS)
25mm
4,000 RPM
Ammunition Container
(181 rounds)

## Slide 31: OCA/DCA
SCL
  DCA 4 x AIM-120
  Future Sidekick 6 x AIM-120
  OCA 2 x AIM-120, 1 x GBU-31, 4 x GBU-39
Playtime
  35.6 to 60 mins

## Slide 32
Questions?
?